## Slide 1: DAFX: Chapter 3 Modulators
Thom Jordan
DSP Spring 2013

## Slide 2
Modulate:
impress a modulator signal onto a carrier signal, by modifying either
the amplitude or phase of the carrier by means of the modulator.

## Slide 3
Ring Modulation:
Notes: In the ring modulation (RM), the audio signal x(n) is multiplied by a sinusoid m(n) with carrier frequency fc.
The input signal is called the modulator x(n) and the second operand is called the carrier m(n), giving the output signal.

## Slide 4
Ring Modulation (sidebands):
Notes: If m(n) is a sine wave of frequency fc, the spectrum of the output y(n) is made up of two copies of the input spectrum: the lower side band (LSB) and the upper side band (USB).
The LSB is reversed in frequency and both side band are centered around fc (see Figure 3.2).
Depending on the width of the spectrum of x(n) and on the carrier frequency, the side bands can be partly mirrored around the origin of the frequency axis. If the carrier signal contains multiple spectral components, the same effect happens with each component.
Although the audible result of a ring modulation is fairly easy to comprehend for elementary signals, it gets very complicated with signals having numerous partials. The carrier itself is not audible in this kind of modulation. When carrier and modulator are sine waves of frequencies fc and fx , one hears the sum and the difference frequencies fc + fx and fc − fx

## Slide 5
Amplitude Modulation:
Notes: The amplitude modulation (AM) was easier to realize with analog electronic means than the ring modulation and has therefore been in use for a much longer time. It can be implemented by
y(n) = [1 + αm(n)] · x(n) (3.2)
where it is assumed that the peak amplitude of m(n) is 1.
The coefficient α determines the modulation depth. The modulation effect is maximum when α = 1 and the effect is disengaged when α = 0. A typical application is with an audio signal as carrier x(n) and a low-frequency oscillator (LFO) as modulator m(n) (see Figure 3.3).
The amplitude of the audio signal varies according to the instantaneous amplitude value of the LFO.
When the modulator is an audible signal and the carrier a sine wave of frequency fc, the spectrum of the output y(t) is similar to that of the ring modulator except that the carrier frequency can be also heard. When carrier and modulator are sine waves of frequencies fc and fx, one hears three components: carrier, difference and sum frequencies (fc −fx, fc, fc +fx).
The effect is perceived in a different manner depending on the frequency range of the signals.
A modulation with frequencies below 20 Hz will be heard in the time domain (variation of the amplitude, tremolo in Figure 3.4), whereas modulations by medium frequencies (20–70 Hz) introduce auditory roughness into the signal.
Modulations by high frequencies will be heard as distinct spectral components (LSB, carrier, USB).

## Slide 6
Single Sideband Modulator:
Notes: The upper and lower side bands of RM and AM carry the same information, although organized differently.
In order to save bandwidth and transmitter power, radio-communication engineers have designed the single-side band (SSB) modulation scheme (Figure 3.5).
Either the LSB or the USB is transmitted. Phase shifted versions by 90◦ of the modulating audio signal x(n) are denoted by xˆ (n) and of the carrier signal m(n) by mˆ (n), and are produced by Hilbert transform filters [Orf96].
The upper and lower side-band signals can be computed as follows:
USB(n) = x(n)m(n) − xˆ(n)mˆ (n) (3.3) LSB(n) = x(n)m(n) + xˆ(n)mˆ (n). (3.4)
After truncation to the desired length N, these coefficients are multiplied with a suitable window function, for example a Hamming window, and shifted right by N−1 to make the filter causal.
Note that the use of the FIR Hilbert filter requires a delay in the direct path for the audio and the carrier signal.

## Slide 7
Notes: Figure 3.6 shows an example with the compensation delay of 30 samples and a FIR Hilbert filter of length N = 61. This effect is typically used with a sine wave as carrier of frequency fc. The use of a complex oscillator for m(n) simplifies the implementation. By using positive or negative frequencies it is then possible to select the USB or the LSB.

## Slide 8
For phase modulation (PM) the phase φ(t) is directly proportional to the modulating signal m(t),
while for frequency modulation the phase φ(t) is the integral of the modulating signal m(t).
The continuous-time description of an angle-modulated carrier signal is given by:
Frequency Modulation:
Notes: The continuous-time description of an angle-modulated carrier signal is given by where Ac is the amplitude of the signal and the argument of the cosine is given by the carrier frequency fc and the modulating signal m(t).
For phase modulation (PM) the phase φ(t) is directly proportional to the modulating signal m(t), while for frequency modulation the phase φ(t) is the integral of the modulating signal m(t).

## Slide 9
Frequency Modulation
vs.
Phase Modulation
Notes: Some examples of frequency and phase modulation are shown in Figure 3.7.
In the first example the modulating signal is a sinusoid which shows that the resulting FM and PM signals are the same except for a time shift in the modulation characteristic.
The second example in (c) and (d) depicts the difference between FM and PM, where the modulating signal is now a bipolar pulse signal.
The last example in (e) and (f) depicts the result of a ramp type signal. The main idea behind using these techniques is the control of the carrier frequency by a modulating signal m(n).
Applying phase modulation to audio signals for audio effects is different from the previous discussion, where a modulating signal m(n) is used to modify the phase φ(t) of a cosine of fixed carrier frequency fc.
By contrast, for audio effects the phase of the audio signal x(n) is modified by a control parameter or modulating signal m(n). The phase modulator system can be described by a time-variant impulse response h(n) and leads to a phase modulated output signal xPM(n)

## Slide 10
Phase Modulation

## Slide 11
Additional example:
Rotary Speaker

## Slide 12: DAFX: Chapter 3 Modulators
Thom Jordan
DSP Spring 2013